## Slide 1: GrailQuest Gamma-ray Astronomy International Laboratory for Quantum Exploration of Space-Time & HERMES High Energy Rapid Modular Ensamble of Satellites Hunting for Gravitational Wave Electromagnetic Counterparts Probing Space-Time Quantum Foam
Luciano Burderi - University of Cagliari
  Tiziana Di Salvo, Andrea Sanna, Fabrizio Fiore, Alessandro Riggio
  On behalf of the HERMES and GrailQuest Collaborations
HERMES
GrailQuest
GrailQuest
Please, visit our websites:
http://hermes.dsf.unica.it
www.hermes-sp.eu

## Slide 2: Two compelling (astro)-physical problems for the next decades
Development of Multi-Messenger astronomy (EM counterparts of GW events)
Is physical space(time) granular or continuous? (Zeno’s paradoxes, existence of a “fundamental minimal length” in some string theories, atoms of space, particles vs. fields, …)
Distributed Astronomy is the key!

## Slide 3
The birth of Multi−Messenger Astronomy
GW170817
NS-NS merging
Host galaxy NGC 4993
~ 40 Mpc
70 observatories

## Slide 4
The Multi−Messenger Astronomy Paradox I
2025+ LIGO/VIRGO/KAGRA/LIGO-INDIA will detect GW170817 within ~ 300 Mpc with localisation accuracy ~10 deg2
FERMI GBM would not have been able to detect GRB 170817A at D > 60 Mpc

## Slide 5
One of he most thrilling research field in Science:
the whole field based on ONE discovery: GRB 170817A - GW170817 connection
Fact ♯ 1:
within 2025 LIGO − Virgo − KAGRA − Einstein Telescope GW antennas will provide detectability of NS−NS mergers events like GW170817 within ≅ 300 Mpc
Localization accuracies:
100 square deg (LIGO − Virgo)
10 square deg (LIGO − Virgo − KAGRA)
Fact ♯ 2:
GBM would not have been able to detect an event 60% fainter than GRB 170817A.
Kilonova events seen at angles ≥ 25 degrees are undetectable by GBM for distances ≥ 60 Mpc.
Fact ♯ 1 + Fact ♯ 2  No EM counterpart detected, no party!
(quoting George Clooney)
We need a All-sky Monitor at least 10÷100×GBM Area for letting Multi−Messenger Astronomy to develop from infancy to maturity!
The Multi−Messenger Astronomy Paradox II

## Slide 6: Long GRB: BH collapse of a massive star
short
long
Short GRB: NS−NS binary
system coalescence
(emission of GW)
GRB progenitors

## Slide 7
Aims:
all Sky Monitor for fast and accurate detection
of the position of bright, transient, high-energy events
and All Sky Monitor of known bright sources (timing):
GRBs
GW events
high-energy counterparts of Fast Radio Bursts
flares from Magnetars
GrailQuest (only)
first dedicated experiment in Quantum Gravity
How:
temporal triangulation of signals detected by a swarm of LEO nano/micro/small satellites equipped with:
keV-Mev scintillators,
sub μs time resolution
temporal triangulation
Pros:
modularity,
limited cost,
quick developement
GrailQuest & HERMES in a nutshell

## Slide 8: Monte-Carlo simulations of a true long GRB
Template (1ms resolution) of a long GRB ( derived from GRB130502327 observed by Fermi GBM) Δt = 40 s; φGRB= 6.5 phot/s/cm2; φBCK= 2.8 phot/s/cm2; variability ≈ 5 ms;
(Long and Short GRB with millisecond time variability, 40% of bright)
zoom of 10 ms of template centered at the main peak
(≈ 5 ms width)

## Slide 9: Accuracy in delays from cross−correlation analysis
Best fit formula:
σDELAYS ≈ σToA = 3.3 μs × (A/1 m2)−0.58
Accuracy in determining delays
from a bright long GRB with
Δt = 40 s;
φGRB= 6.5 phot/s/cm2;
φBCK= 2.8 phot/s/cm2;
variability timescale ≈ 5 ms;
1000 pair of Monte-Carlo simulations
for detectors of different effective
areas A

## Slide 10
GW Triangulation & EM counterparts
(Fermi GBM, INTEGRAL, HERMES Pathfinder)
Example:
long bright GRB
6.5 phot/s/cm2 (source)
3 phot/s/cm2 (background)
30 s duration
50-300 keV band
3 satellites each of
effective area: 50 cm2
σToA ≈ 1 ms
<baseline> ≈ 6000 km
positional accuracy: 3 deg

## Slide 11: Quantum Gravity Minimal Length Hypotesis, LIV and Dispersion Relation for photons in vacuo
Existence of a Minimal Length (String theories, etc.)
lMIN ≈ lPLANCK = [Gh/(2πc3)]1/2 = 1.6 × 10-33 cm
implies:
Lorentz Invariance Violation (LIV): no further Lorentz contraction
Space has the structure of a crystal lattice and therefore
Existence of a dispersion law for photons in vacuo
|vphot/c − 1| ≈ ξ Ephot/(MQG c2)n
ξ ≈ 1
n = 1,2 (first or second order corrections)
MQG = ζ mPLANCK (ζ ≈ 1)
mPLANCK = (hc/2πG)½ = 21.8 10−6 g
lMIN ≈ lPLANCK

## Slide 12: First and second order Dispersion Relation for photons in vacuo
First Order Dispersion Relation
vphot/c ≈ 1 - ξ Ephot/(MPlanck c2)
Second Order Dispersion Relation
vphot/c ≈ 1 - ξ [Ephot/(MPlanck c2)]2
/c4
Loop Quantum Gravity (Rovelli)
No LIV theories
LIV theories
Space−Time
Uncertainty Relation Δr Δt > Għ/c4
& Sanchez,
2018
Burderi, Di Salvo, Iaria (2016)
lMIN ≈ lPLANCK

## Slide 13: Dispersion Relation for photons in vacuo and Delays in travel time
Accumulation of delays in light propagation:
ΔtMP/LIV = ξ (DTRAV/c) [ΔEphot/(MQG c2)]n
The distance traveled by photons takes into account the cosmological expansion:
DTRAV(z)=(c/H0)0z dβ (1+β)/[ΩΛ+(1+β)3 ΩM]1/2
z: cosmological redshift
ΩΛ: ratio between the energy density due to the cosmological constant and the critical (closure) density of the Universe
ΩM: ratio between the energy density due to the matter and the critical (closure) density of the Universe

## Slide 14: The Energy & Redshift delay
Time lags caused by Quantum Gravity effects:
   |Ephot(Band II)−Ephot(Band I)|
   DGRB(zGRB)
Time lags caused by prompt emission mechanism:
  complex dependence from Ephot(Band II) and Ephot(Band I)
  independent of DGRB(zGRB)
High z
Low z

## Slide 15: GRBs & Quantum Gravity
σCC ≈ 0.46 μsec × (2.6 108/N)0.5
ΔtMP/LIV = ξ (DTRAV/c) [ΔEphot/(MQG c2)]n
DTRAV(z)=(c/H0)0z dβ (1+β)/[ΩΛ+(1+β)3 ΩM]1/2

## Slide 16: Location of GRBs with fleets of satellites and redshifts
Accuracy in determining delays from Monte-Carlo simulations of 100 pairs of GRBs of fluence 260 (112 BCK) photons/cm2 with detectors of different effective areas:
σDELAYS ≈ σToA = 3.3 μs × (A/1 m2)−0.58
Accuracy in determining α and δ with NSATELLITES (NIND = NSATELLITES − 1; NPAR= 2):
σα ≈ σδ = c σToA/<baseline> × (NIND − NPAR)−1/2
Large fleet of small satellites in Low Earth Orbits:
A = 30 × 30 cm ≈ 0.1 m2
σToA ≈ 12.5 μs
NSATELLITES ≈ 1000
<baseline> ≈ 6,000 km
σα ≈ σδ ≈ 4 arcsec
Three satellites with detectors of 1 m2 effective area in Earth−Moon Lagrangian points
MEANS (Moon-Earth Array of Nano Satellites) Project:
A ≈ 1.0 m2
σToA ≈ 3.3 μs
NSATELLITES = 3
<baseline> ≈ 400,000 km
σα ≈ σδ ≈ 0.5 arcsec
Once the position is known, the redshift of the GRB host galaxy is obtained through pointed observations of large optical telescopes.

## Slide 17: MEANS: Moon-Earth Array of NanoSats
MEANS: Phase A/B study (cost 1.18 M€) ASI call 2020
Università di Cagliari, INAF, ARGOTEC,
Politecnico di Milano, Fondazione Bruno Kessler, Università di Palermo
A ≈ 1.0 m2
σToA ≈ 3.3 μs
NSATELLITES = 3
<baseline> ≈ 400,000 km
σα ≈ σδ ≈ 0.5 arcsec

## Slide 18: GrailQuest: First Quantum-Gravity dedicated experiment
Δt~μs
ΔT~Gyr
Robust Quantum Gravity Experiment to:
i) Search for a Dispersion law for photons vph/c ~ [1-lP/λph]
ii) Explore Space−Time Granular structure down to lP~10-33 cm
Performed by means of a Constellation of 100÷10000 small sats with: i) Total collecting area: ~100 m2
ii) Energy band: 50 keV − 50 MeV
iii) Time resolution: < 0.1 μs
In a nutshell:

## Slide 19: GrailQuest selected for the 2019 Call for White Papers for the Voyage 2050 long term plan in the ESA Science Programme
Δt~μs
ΔT~Gyr
In a nutshell:
Download paper at arXiv:1911.02154v2

## Slide 20: HERMES Next Generation − OneWeb
OneWeb Constellation 650 sats
Virgin Galactic (Richard Branson) − Arianespace − Airbus Defence and Space
640 @ 1200 km
150 kg satellites (mass production)
110 satellites launched at 18/12/2020
board a 30×30 = 900 cm2 effective area detector (e.g. GAGG crystal − SDD photodetector + position sensitive with coded mask?) on each satellite
60 m2 effective area All Sky Monitor
GrailQuest Next Generation − OneWeb symbiont

## Slide 21: GrailQuest Next Generation − Starlink symbiont
Starlink Constellation 12,000 sats
SpaceX (Elon Musk)
4425 @ 1200 km (completed by 2024)
955 satellites launched at 25/11/2020
7518 @ 340 km
up to 1,000,000 fixed satellite earth stations
optical inter−satellite links
100 ÷ 500 kg satellites (mass production)
board a 10×10 = 100 cm2 effective area detector (e.g. GAGG crystal − SDD photodetector + position sensitive with coded mask?) on each satellite
120 m2 effective area All Sky Monitor!

## Slide 22: GrailQuest Next Generation − Kuiper System symbiont
Philantropy in Astronomy
Hale reflector (5.1 m diameter) in Palomar Observatory funded by Rockfeller Foundation in 1928 proposed by George Ellery Hale
From prototypes to industrial manufacturing
Mass production (cut of costs, great intuition of Henry Ford, inventor of the Assembly Line)
Amazon’s Kuiper System Satellites 3,236 sats
Amazon & Blue Origin(?) (Jeff Bezos)
April 2019

## Slide 23
That’s all Folks!
Please, visit our websites:
http://hermes.dsf.unica.it
www.hermes-sp.eu